## Slide 1: Introduction to Fadecandy
ILD 6th of April 2016

## Slide 2: What’s in the kits
Fadecandy
Power cables
Neopixel 8x8 matrix
LED Strip

## Slide 3: Setup
(source: https://github.com/scanlime/fadecandy)

## Slide 4: Getting started
Download the library from https://github.com/scanlime/fadecandy
Run the server from the Terminal (Mac)
  cd ~/Downloads/fadecandy-master/bin
  open fcserver-osx
Open the fadecandy-master/bin folder and run fcserver.exe (windows)
Open Processing and run your program.

## Slide 5: Creating a new program
Open Pixel Control (OPC)
Define screen size
Setup the server connection
Define LED type
  Port
  Midpoint
  Spacing
  Rotation
  Direction

## Slide 6: Changing individual pixels
setPixel(index, color);
opc.setPixel(0, color(255,0,0));
for (int i = 0; i < 8; i++) {
  opc.setPixel(i+8*0, color(255,0,0));
  opc.setPixel(i+8*1, color(0,255,0));
  opc.setPixel(i+8*2, color(0,0,255));
  opc.setPixel(i+8*3, color(127,0,0));
  opc.setPixel(i+8*4, color(0,127,0));
  opc.setPixel(i+8*5, color(0,0,127));
  opc.setPixel(i+8*6, color(100,100,100));
  opc.setPixel(i+8*7, color(200,200,200));
}
opc.writePixels();

## Slide 7: Webserver
http://localhost:7890
Number specified in your code
Make sure the server is running
Turn off all LEDs
Test LEDs
Identify Fadecandy

## Slide 8: Premade Examples (dot)

## Slide 9: Premade Examples (noise)

## Slide 10: Premade Examples (orbit)

## Slide 11: Premade Examples (wavefront)

## Slide 12: 3D Printed Covers
(no cover)
(transparent PLA)
(white PLA)

## Slide 13: 3D Printed Covers